BLISS Model ED-4460, 60 “Wide Screen X 44 “ Rotor with dual Motor

Web Site & Specification: http://www.bliss-industries.com/htm/hmill.htm

Screen : 7,200 sq.in of working area.

Max. HP : 400 HP X 1750 RPM

Tip Speed: 20,735 FPM (Ideal for fibrous material)

Capacity: Base on a conversation with Mr. Jason Bliss of Bliss Industries, Ponca City,

OK, Usa. Sept-7-2006. Calculation: IF x HP x Screen size (64”) = lbs/hrs.

# Wood Shaving @ 45 % H2O @ 4 Index Factor

3/8“ Screen, 300 HP - 1750 RPM…………………....................15 ton/hrs.

3/8“ Screen, 400 HP – 1750 RPM ..............................................18 Ton/hrs.

½ “ Screen, 300 HP – 1750 RPM .................……………..........18 Tons/hrs.

½ “ Screen, 400 HP – 1750 RPM …………………………...…21 Ton/hrs

½ “ Wood Particle size @ 10 % H2O @ 8 Index Factor

5/16 “- ¼ “ Screen, 300 HP – 1750 RPM……………..………..18 ton/hrs.

5/16 “- ¼ “ Screen, 400 HP – 1750 RPM...........................…… 23 ton/hrs

Hammer Mill proposed Installation :

Air releif assist Negatif Product Conveying. Calculated by the distance to travel.

Air Relief Assist w/ Bag Filter, Plenum chamber and Screw Convoyer.

Required 1 CFM/inch of screen working area 0r 7,200 CFM.

Air Releif Assist w/ Cyclone Separator, Plenum chamber and Screw Convoyer.

Required 1 CFM/inch of screen working area 0r 7,200 CFM.

** Ref: http://www.bliss-industries.com/pdfs/condmill.pdf

Note: Price NEW from Bliss Ind., $ 65,000.00 Less Motor and less Pocket Feeder.

FOB: OK, Usa

Regards,

Yvon L. Roy, Pdg

Processco Inc.